## Slide 1: VTT7 Intro til mikrosimulering og SUMO
Kursusgang 10

## Slide 2: Plan for today
Goals:
Get familiar with SUMO Traffic Control Interface (TraCI)
You have already done:
Go through the solutions to exercise 1 and 2 and prepare questions if something was unclear.
Get introduced to Traffic Control Interface (TraCI) following the tutorial here
Lecture 10 - Advanced SUMO
Lecture 7 exercise review
Introduction to TraCI and example walkthrough
Exercise

## Slide 3: TraCI
TraCI - Traffic Control Interface to write automated procedures for SUMO
https://sumo.dlr.de/docs/TraCI.html
https://sumo.dlr.de/docs/TraCI/Interfacing_TraCI_from_Python.html
Potential tasks:
Running a batch of simulations sequentially or in parallel on multiple computers
Interacting with traffic during simulation to
  Customize car following models
  Introduce novel intelligent routing / traffic control algorithms
  Exchange information with other programs / services
On par with sumolib create your own sumo tools similar to https://sumo.dlr.de/docs/Tools/index.html
Comes together with SUMO installation and can be added to your python script with
import traci

## Slide 4: TraCI
TraCI commands:
https://sumo.dlr.de/docs/TraCI.html#traci_commands
namespaces: https://sumo.dlr.de/pydoc/traci.html
gui, simulation
person, vehicle, vehicletype
lane, edge, poi, junction, polygon, route
trafficlight, variablespeedsign
inductionloop, lanearea, multientryexit
For each namespace (topic) you can either get a specific value (vehicle speed, traffic light state, etc) for this timestep or change it in the next timestep, for example:
traci.trafficlight.setPhase(‘C’, 0)
module/ library
namespace
Specific function in the namespace with its parameters

## Slide 5: TraCI
Walkthrough of a simple TraCI program from https://github.com/TRG-BUILD/sumo_course/tree/master/course2021/part3_automation/example1
runner.py
runner_multiple.py
Walkthrough of an actuated traffic control TraCI code:
https://intelaligent.github.io/tctb/post-learning-traci-tls.html
How would you make cars coming more often?
How would you make cars coming with Poisson distribution?
How would you make cyclists?

## Slide 6: Exercise
Pick any intersection you have done with SUMO:
Create python code that lets you run the simulation:
  Once with sumo-gui command
  Once with sumo command
  5 times with sumo command
Run simulation once with sumo. For each timestep use the documentation, calculate and print out:
  The number vehicles present in the intersection
  Average speed of all vehicles
  Queue length on each approach edge
  Generate tripinfo output on each run with a unique name containing the run number
For the fast:
Run simulation 5 times, collect average speeds and queue length for each timestep and save as a CSV file

## Slide 7: Summary: What have we learnt today?
How to call SUMO simulation step by step from python that forms a basis of most advanced applications of SUMO
How to inject our own logic into the simulation
How to run multiple SUMO simulations in a row
How to generate your own customized demand files from python

## Slide 8: Important topics we have not covered
Calibration with real data
https://sumo.dlr.de/docs/Simulation/Calibrator.html
https://sumo.dlr.de/docs/Tutorials/Calibration/San_Pablo_Dam.html
Interaction with OSM:
https://sumo.dlr.de/docs/Tutorials/OSMWebWizard.html
https://sumo.dlr.de/docs/Tutorials/port.html
Public transport stops and traffic:
https://sumo.dlr.de/docs/Tutorials/PublicTransport.html
Case studies:
https://sumo.dlr.de/docs/Tutorials/#sumo_user_conference